## Slide 1: Existing Building Commissioning Workshop Series 16, May 6, 2021
Energy Calculations – Part 2
David Sellers
Senior Engineer, Facility Dynamics Engineering
Presented By:

## Slide 2: Review

## Slide 3: How Pumps Use Energy

## Slide 4: Observation 1
A field clue reveals the opportunity to save pump run hours by returning the selector switch to “Auto” for the lead pump

## Slide 5: Let’s Explore That
A field clue reveals the opportunity to save pump run hours by returning the selector switch to “Auto” for the lead pump

## Slide 6: Observation 2
A field clue reveals the opportunity to save 12 ft.w.c. in pump head if the pump can be optimized by some other means besides throttling
Throttling probably saved some energy

## Slide 7: Lets Explore That
A field clue reveals the opportunity to save 12 ft.w.c. in pump head if the pump can be optimized by some other means besides throttling
Throttling probably saved some energy

## Slide 8: Pump Optimization Options - Throttling
Increasing Flow
Increasing Head
Notes: H F
7.84 8.00
6.00 7.00
3.06 5.00
1.10 3.00
0.49 2.00
0.12 1.00
0.00 0.00

## Slide 9: Pump Optimization Options – Trim Impeller
Increasing Flow
Increasing Head
Notes: H F
7.84 8.00
6.00 7.00
3.06 5.00
1.10 3.00
0.49 2.00
0.12 1.00
0.00 0.00

## Slide 10: Pump Optimization Options – Reduce Speed
Increasing Flow
Increasing Head
Notes: H F
7.84 8.00
6.00 7.00
3.06 5.00
1.10 3.00
0.49 2.00
0.12 1.00
0.00 0.00

## Slide 11: Pump Optimization Options – Right Sizing
Increasing Flow
Increasing Head
Notes: H F
7.84 8.00
6.00 7.00
3.06 5.00
1.10 3.00
0.49 2.00
0.12 1.00
0.00 0.00

## Slide 12: The Assignment

## Slide 13: The Assignment
Assess the savings for all the options for the Chiller 2 evaporator pump
  Not all of them may be viable
Once you have identified the viable options, e-mail me for bids for doing the work
  Don’t wait until the last minute!
Develop the simple payback for each option
Select the option you would ultimately choose for each Owner type and explain why
Perform the assessment for the following locations
Honolulu, HI
  $0.2917 per kWh electricity
San Francisco, CA
  $0.1621 per kWh electricity
Sacramento, CA
  $0.1331 per kWh electricity
St. Louis, MO
  $0.0571 per kWh electricity

## Slide 14: The Assignment
Assess the savings for all the options for the Chiller 2 evaporator pump
  Not all of them may be viable
Once you have identified the viable options, e-mail me for bids for doing the work
Develop the simple payback for each option
Select the option you would ultimately choose and explain why
Perform the assessment for the following locations
Honolulu, HI
  $0.2917 per kWh electricity
San Francisco, CA
  $0.1621 per kWh electricity
Sacramento, CA
  $0.1331 per kWh electricity
St. Louis, MO
  $0.0571 per kWh electricity

## Slide 15: The Assignment
Perform the assessment for the following locations
Breakout A - Honolulu, HI
  $0.2917 per kWh electricity
Breakout B - San Francisco, CA
  $0.1621 per kWh electricity
Breakout C - Sacramento, CA
  $0.1331 per kWh electricity
Breakout D - St. Louis, MO
  $0.0571 per kWh electricity

## Slide 16: Owner Types/Financial Metrics
Owner 1 - Investment fund for a teachers union retirement fund - 5 year simple payback window, in-house control work capabilities.
Owner 2 - Real Estate investment portfolio - 2 year simple payback window, all modification work is out of house.
Owner 3 - Personal investment, 8 year simple payback window for central plant equipment, all modification work is out of house.
Owner 4 - Personal investment, 10 year simple payback window for central plant equipment. Capital Budget has upcoming projects to add redundant evaporator, condenser and distribution chilled water pumps - same make and model as existing - this year and redundant chiller and cooling tower next year.

## Slide 17: An Assumption
Assume the plant can be shut down when the outdoor temperature is below 51°F

## Slide 18: Presenting Your Results
One Team will present their results during the next webinar
Informal presentation
Ryan will ask for a volunteer ahead of time
No volunteers means Ryan picks someone at random at the next during the next webinar
If your team volunteers, everyone on the team gets a datalogger
You will not know if anyone has volunteered (so be ready to present)

## Slide 19: Resources

## Slide 20: Resources

## Slide 23: Pump Speed

## Slide 24: Other Resources
Square Law Tool
    http://www.av8rdas.com/affinity-laws.html
Affinity Law Information
    http://www.av8rdas.com/affinity-laws.html
  Affinity Law Tools
    Flow and Impeller Diameter Relationship
      http://www.av8rdas.com/affinity-laws.html#Diameter
    Flow and Impeller Speed Relationship
      http://www.av8rdas.com/affinity-laws.html#Speed
    Power and Impeller Speed Relationship
      http://www.av8rdas.com/affinity-laws.html#Power

## Slide 25: Other Resources
Pump Selection Tool
    http://bellgossett.com/selection-sizing-cad-tools/

## Slide 26: Other Resources
Pick the “ESP-Systemwize” link and you will be taken to a data entry screen for pumps

## Slide 27: Other Resources
Enter your selection criteria

## Slide 28: Other Resources
Select “Get Results”

## Slide 29: Other Resources
Page down to see your options