## Slide 1: Break Out Guidance
Developing Findings and Energy Calculations
David Sellers; Facility Dynamics Engineering
Senior Engineer

## Slide 2: Breakout 01
Given
Ball Room AHU Model
Drawings
  System Diagram
  Equipment Schedule
  Point List/Narrative Sequence
Operator Discussions
Assignment
Scope out the Ball Room AHU to identify potential opportunities to improve performance and save resources

## Slide 4: Breakout 02
Given
The minimum outdoor air setting
The economizer high limit setting
An assumption that warm-up is accomplished by the reheat coils
A typical operating schedule (next slide)
The weather data resources we discussed
Field observations of the system operating parameters
Assignment
Determine the number of hours the heating coil may need to function
Determine the number of hours a year the observed HW coil temperature rise is a false load
Determine the number of hours a year the false load becomes a chilled water false load

## Slide 5: Ball Room AHU Typical Schedule
Monday – Friday 6:00 AM – 10:00 PM
Saturday – 3:00 PM – Midnight
Sunday – 9:00 AM – 3:00 PM

## Slide 6
https://www.screencast.com/t/N75JtXeNNpuIhttps://www.screencast.com/t/N75JtXeNNpuI

## Slide 7: Breakout 03
Given
Field observations
The District Steam Tariff
EnergyStar Conversion Factors
Assignment
Identify the thermal energy waste for the current hour of operation
How many tons of false load is this putting on the chilled water plant?
What are the possible causes of the undesired HW coil temperature rise?
Consider the questions in the next slide

## Slide 8: Break Out 03 Questions
Does boiler system thermal efficiency come into play with the district steam thermal source?
How would your conclusions regarding energy waste be impacted if the HW system was served by a conventional boiler like the Lochinvar CopperFin product?
How would your conclusions regarding energy waste be impacted if the HW system was served by a condensing boiler like the Aerco Benchmark product?

## Slide 10: Breakout 04
Given
Mixed air plenum test results
Assignment
Determine the true mixed air temperature?
What is the actual system flow rate?
Adjust your thermal savings projection for the hour based on this information
How many tons of load on the chilled water plant are due to the current economizer dysfunction?