## Slide 1: Existing Building Commissioning Workshop: Series 17, 2022-02-10
Cooling Tower Optimization Mystery
David Sellers
Senior Engineer, Facility Dynamics Engineering
Presented By:

## Slide 2: Given Previous Discussions

## Slide 3: Given Previous Discussions

## Slide 4: Given Previous Discussions

## Slide 5: And Related Costs/Benefit Potential

## Slide 6: And a Similar Opportunity at the Hijend Hotel

## Slide 7: And a Similar Opportunity at the Hijend Hotel

## Slide 8: And a Similar Opportunity at the Hijend Hotel

## Slide 9: And a Similar Opportunity at the Hijend Hotel

## Slide 10: And a Similar Opportunity at the Hijend Hotel

## Slide 11: Along with the Following Information
Hijend Hotel Models or Images
CW System Diagram
Cooling Tower Dimensions
  Hot Basin
    Operating Depth – 7-1/2”
    Length – 13’ 6-1/2”
    Width – 4’ 4-3/8”
  Cold Basin
    Length – 21’ 9”
    Width – 13’ 6-3/4”
    Sump Width – 2’ 9-5/8”
    Sump Depth – 3-7/8”
    Overflow Depth at Sump – 1’ 2-3/8”
12’ of 8” hot basin CWR connection pipe above the hot basin water level
4” Minimum recommended water level (at sump)

## Slide 12: Answer the Following Questions
What needs to be considered to set the following water levels for your control system
  Overflow alarm?
  Low level alarm?
  Open the make-up valve?
  Close the make-up valve?
What would your recommendations be for the appropriate operating levels for:
  Overflow alarm?
  Low level alarm?
  Open the make-up valve?
  Close the make-up valve?
Are their any issues that would need to be addressed to ensure success in terms of not wasting water after your new level control system is in place?