## Slide 1: System Diagrams
Symbol Library – Black Background
David Sellers
Facility Dynamics Engineering
2015-11-06

## Slide 2: Notes
The symbols are set up for a 0.10 inch grid
To get things to line up, the symbols need to be symmetric around the alignment axis. To get that to happen there are “hidden” parts in the symbols. The hidden parts are set to the same color as the background, which is what “hides” them. For example, on a black background, this plug valve symbol appears as follows.
But on a non-black background, you would see this.
The black line is what will cause the symbol to line up vertically with the middle of something else if you pick the “Align – Center” option. The horizontal alignment (“Align – Middle”) will happen with out an extra hidden line since the symbol size is an even multiple of -.10 inches in the vertical direction.
The reason that you have to do this (assuming you want things to line up on the grid, which is a good practice) is that the “Align – Middle” and “Align – Center” commands align all of the selected objects based on the average of their initial positions. So, that needs to be some even multiple of the grid spacing.
Even then, the alignments may put you in the middle of a grid reference. But once the objects are aligned to that point, if you keep them highlighted and use the arrow keys (with the snap to grid feature on), they will snap to the nearest grid point and end up on the grid.

## Slide 3: Water Systems

## Slide 4: Piping
Plug Valve
Check Valve
Butterfly Valve
Venturi Check Valve
Flow Venturi
Gate Valve
Ball Valve
Balance Valve
Triple Duty Valve
Strainer with Blow Down Valve
Suction Diffuser
Gauge
Thermometer in Well
Thermometer Well
Flow Switch
FlSw
Fan Coil Solenoid Valve
Fan Coil Service Valve
2-Way Control Valve
Pressure Reducing Valve
Pressure Relief Valve
3-Way Control Valve
TT
Temperature Transmitter
PT
Pressure Transmitter

## Slide 5: Piping
Triple Duty Valve
Butterfly Valve
Gate Valve
Ball Valve

## Slide 6: Piping
Triple Duty Valve

## Slide 7: Equipment
Chiller ???
Make and Model
Cool ?,??? gpm from ??°F to ??°F using ?,??? Gpm of ??° condenser water
??? kW at full load
Evaporator
Condenser
Centrifugal Chiller
Plate and Frame Heat exchanger

## Slide 8: Equipment
Pump
Pump ???
Make and Model
?,??? gpm at ?? ft.w.c.
?,??? rpm
?? hp
?? bhp

## Slide 9: Equipment
Pump
Pump ???
Make and Model
?,??? gpm at ?? ft.w.c.
?,??? rpm
?? hp
?? bhp
Air Separator
Cold water make-up from a back flow preventer
Expansion Tank with Make-up

## Slide 10: Equipment
Pump ???
Make and Model
?,??? gpm at ?? ft.w.c.
?,??? rpm
?? hp
?? bhp
DP
Pump with service valves and check valve
Heat Exchanger
Heat Exchanger 1
LPS
LPR

## Slide 11: Equipment
Finned Tube Radiation Load
Outdoor Air AHU

## Slide 12: Equipment
Domestic Hot Water Storage Tank and Heater
Boiler ???
Make and Model
Heat ?,??? gpm from ??°F to ??°F

## Slide 13: Equipment
Forced Draft Cooling Tower
Cooling Tower ????
Make and Model
???,???,??? Btu/hr heat rejection
??/?? hp/bhp fan at ?,??? Rpm
??/?? °F Entering/Leaving Water Temperature at ??°F twb
Cooling Tower ????
Make and Model
???,???,??? Btu/hr heat rejection
??/?? hp/bhp fan at ?,??? Rpm
??/?? °F Entering/Leaving Water Temperature at ??°F twb
Induced Draft Cooling Tower

## Slide 14: Pumped Preheat Coil
Corridor Make-up Unit Preheat Coil
Corridor Make-up Unit Preheat Coil
Coil Circulation Pump
Make and Model
?,??? gpm at ?? ft.w.c.
?,??? rpm
?? hp
?? bhp
Corridor Make-up Unit Preheat Coil
Corridor Make-up Unit Preheat Coil
Heating Coil 1
??,??? cfm
Entering air - ??.?°F
Leaving air - ??.?°F
Airside ∆p - ??.? in.w.c.
??? Gpm
Entering water - ??.? °F
Leaving water - ??.? °F
Waterside ∆p - ??.? ft.w.c.
Maximum face velocity – 500 fpm
Minimum rows - ?

## Slide 15: Heating Coil
Typical Air Handling Unit Heating Coil
Typical Air Handling Unit Heating Coil
Heating Coil 1
??,??? cfm
Entering air - ??.?°F
Leaving air - ??.?°F
Airside ∆p - ??.? in.w.c.
??? Gpm
Entering water - ??.? °F
Leaving water - ??.? °F
Waterside ∆p - ??.? ft.w.c.
Maximum face velocity – 500 fpm
Minimum rows - ?

## Slide 16: Heating Coils – Typical Circuit
Typical Coil
??? cfm
Entering air - ??.?°F
Leaving air - ??.?°F
Airside ∆p - ??.? in.w.c.
??? Gpm
Entering water - ??.? °F
Leaving water - ??.? °F
Waterside ∆p - ??.? ft.w.c.
Maximum face velocity – 500 fpm
Minimum rows - ?
Typical Meeting Room Reheat Coil
Typical Meeting Room Reheat Coil
Total Flow for the Branch - ??? gpm

## Slide 17: Cooling Coil
Typical Air Handling Unit
Typical Air Handling Unit
Cooling Coil 1
??,??? cfm
Entering air - ??.?°F tdb
Entering air - ??.?°F twb
Leaving air - ??.?°F tdb
Leaving air - ??.?°F twb
Airside ∆p - ??.? in.w.c.
??? Gpm
Entering water - ??.? °F
Leaving water - ??.? °F
Waterside ∆p - ??.? ft.w.c.
Maximum face velocity – 500 fpm
Minimum rows - ?

## Slide 18: Cooling Coils – Typical Circuit
Total Flow for the Branch - ??? gpm
Typical Guest Room Fan Coil
Typical Guest Room Fan Coil
Typical Guest Room Floor
Cooling Coil 1
??,??? cfm
Entering air - ??.?°F tdb
Entering air - ??.?°F twb
Leaving air - ??.?°F tdb
Leaving air - ??.?°F twb
Airside ∆p - ??.? in.w.c.
??? Gpm
Entering water - ??.? °F
Leaving water - ??.? °F
Waterside ∆p - ??.? ft.w.c.
Maximum face velocity – 500 fpm
Minimum rows - ?

## Slide 19: Air Systems

## Slide 20: Equipment
Propeller Fan
AHU-1
??,??? cfm at ??.? in.w.c.
??% static efficiency
?,??? rpm, Class ?
??.? bhp, ?? hp motor
EF-1
??,??? cfm at ??.? in.w.c.
??% static efficiency
?,??? rpm, Class ?
??.? bhp, ?? hp motor
Lab Hood

## Slide 21: Economizer Section, Louver
?,??? cfm Minimum Outdoor Air
??,??? cfm Maximum Outdoor Air
??,??? cfm Relief Air
??,??? cfm Return Air
??,??? cfm Mixed Air
NC Min. OA Damper
NO Return Air Damper
NC Relief Air Damper
NO Max. OA Damper
Louver

## Slide 22: Filters, Dampers
High Efficiency Filter Bank
Low Efficiency Filter Bank/Prefilter Bank
8 – 24” x 24” x 12”
MERV 13 Filters
Clean ∆p = 0.15 in.w.c.
Dirty ∆p = 0.90 in.w.c.
8 – 24” x 24” x 2”
MERV 7 Filters
Clean ∆p = 0.07 in.w.c.
Dirty ∆p = 0.50 in.w.c.
Normally Open (N.O.) Parallel Blade Damper
Normally Closed (N.C.) Parallel Blade Damper
Normally Open (N.O.) Opposed Blade Damper
Normally Closed (N.C.) Opposed Blade Damper

## Slide 23
Fans
VFD
VFD
Fans

## Slide 24: Filters, Dampers
Barometric Damper

## Slide 25: Coils
Cooling Coil 1
??,??? cfm
Entering air - ??.?°F tdb
Entering air - ??.?°F twb
Leaving air - ??.?°F tdb
Leaving air - ??.?°F twb
Airside ∆p - ??.? in.w.c.
??? Gpm
Entering water - ??.? °F
Leaving water - ??.? °F
Waterside ∆p - ??.? ft.w.c.
Maximum face velocity – 500 fpm
Minimum rows - ?
Cooling Coil 1
??,??? cfm
Entering air - ??.?°F tdb
Entering air - ??.?°F twb
Leaving air - ??.?°F tdb
Leaving air - ??.?°F twb
Airside ∆p - ??.? in.w.c.
??? Gpm
Entering water - ??.? °F
Leaving water - ??.? °F
Waterside ∆p - ??.? ft.w.c.
Maximum face velocity – 500 fpm
Minimum rows - ?
Heating Coil 1
??,??? cfm
Entering air - ??.?°F
Leaving air - ??.?°F
Airside ∆p - ??.? in.w.c.
??? Gpm
Entering water - ??.? °F
Leaving water - ??.? °F
Waterside ∆p - ??.? ft.w.c.
Maximum face velocity – 500 fpm
Minimum rows - ?
Heating Coil 1
??,??? cfm
Entering air - ??.?°F
Leaving air - ??.?°F
Airside ∆p - ??.? in.w.c.
??? Gpm
Entering water - ??.? °F
Leaving water - ??.? °F
Waterside ∆p - ??.? ft.w.c.
Maximum face velocity – 500 fpm
Minimum rows - ?

## Slide 26: Evaporative Cooler
Direct Evaporative Cooler
??,??? cfm
Entering air - ??.?°F tdb
Entering air - ??.?°F twb
Leaving air - ??.?°F tdb
Leaving air - ??.?°F twb
Airside ∆p - ??.? in.w.c.
??? Gpm
Maximum face velocity – 500 fpm

## Slide 27: Loads
Fan Coil Unit
(Typical)
Nominal 500 cfm

## Slide 28: Common

## Slide 29: Match Line
Match Line – See Sheet 2
A
B
C
D